## Slide 1: William Stallings Computer Organization and Architecture 9th Edition
Notes: Lecture slides prepared for “Computer Organization and Architecture”, 9/e, by William Stallings, Chapter 5 “Internal Memory”.

## Slide 2: Chapter 5
Internal Memory
Notes: We begin this chapter with a survey of semiconductor main memory subsystems,
including ROM, DRAM, and SRAM memories. Then we look at error control
techniques used to enhance memory reliability. Following this, we look at more
advanced DRAM architectures.

## Slide 3: Memory Cell Operation
Notes: In earlier computers, the most common form of random-access storage for computer
main memory employed an array of doughnut-shaped ferromagnetic loops
referred to as cores. Hence, main memory was often referred to as core, a term that
persists to this day. The advent of, and advantages of, microelectronics has long
since vanquished the magnetic core memory. Today, the use of semiconductor chips
for main memory is almost universal. Key aspects of this technology are explored
in this section.
The basic element of a semiconductor memory is the memory cell. Although a variety
of electronic technologies are used, all semiconductor memory cells share certain
properties:
• They exhibit two stable (or semistable) states, which can be used to represent
binary 1 and 0.
• They are capable of being written into (at least once), to set the state.
• They are capable of being read to sense the state.
Figure 5.1 depicts the operation of a memory cell. Most commonly, the cell
has three functional terminals capable of carrying an electrical signal. The select
terminal, as the name suggests, selects a memory cell for a read or write operation.
The control terminal indicates read or write. For writing, the other terminal
provides an electrical signal that sets the state of the cell to 1 or 0. For reading, that
terminal is used for output of the cell’s state. The details of the internal organization,
functioning, and timing of the memory cell depend on the specific integrated
circuit technology used and are beyond the scope of this book, except for a brief
summary. For our purposes, we will take it as given that individual cells can be
selected for reading and writing operations.

## Slide 4: Semiconductor Memory Types
Table 5.1 Semiconductor Memory Types
Notes: All of the memory types that we will explore in this chapter are random access. That is,
individual words of memory are directly accessed through wired-in addressing logic.
Table 5.1 lists the major types of semiconductor memory. The most common
is referred to as random-access memory (RAM). This is, in fact, a misuse of the
term, because all of the types listed in the table are random access. One distinguishing
characteristic of memory that is designated as RAM is that it is possible
both to read data from the memory and to write new data into the memory easily
and rapidly. Both the reading and writing are accomplished through the use of
electrical signals.
The other distinguishing characteristic of RAM is that it is volatile. A RAM
must be provided with a constant power supply. If the power is interrupted, then
the data are lost. Thus, RAM can be used only as temporary storage. The two traditional
forms of RAM used in computers are DRAM and SRAM.

## Slide 5: Dynamic RAM (DRAM)
RAM technology is divided into two technologies:
  Dynamic RAM (DRAM)
  Static RAM (SRAM)
  DRAM
    Made with cells that store data as charge on capacitors
    Presence or absence of charge in a capacitor is interpreted as a binary 1 or 0
    Requires periodic charge refreshing to maintain data storage
    The term dynamic refers to tendency of the stored charge to leak away, even with power continuously applied
Notes: RAM technology is divided into two technologies: dynamic and
static. A dynamic RAM (DRAM) is made with cells that store data as charge on
capacitors. The presence or absence of charge in a capacitor is interpreted as a
binary 1 or 0. Because capacitors have a natural tendency to discharge, dynamic
RAMs require periodic charge refreshing to maintain data storage. The term
dynamic refers to this tendency of the stored charge to leak away, even with power
continuously applied.

## Slide 6: Dynamic RAM Structure
Figure 5.2a
Typical Memory Cell Structures
Notes: Figure 5.2a is a typical DRAM structure for an individual cell that stores 1 bit.
The address line is activated when the bit value from this cell is to be read or written.
The transistor acts as a switch that is closed (allowing current to flow) if a voltage is
applied to the address line and open (no current flows) if no voltage is present on
the address line.
For the write operation, a voltage signal is applied to the bit line; a high voltage
represents 1, and a low voltage represents 0. A signal is then applied to the
address line, allowing a charge to be transferred to the capacitor.
For the read operation, when the address line is selected, the transistor turns
on and the charge stored on the capacitor is fed out onto a bit line and to a sense
amplifier. The sense amplifier compares the capacitor voltage to a reference value
and determines if the cell contains a logic 1 or a logic 0. The readout from the cell
discharges the capacitor, which must be restored to complete the operation.
Although the DRAM cell is used to store a single bit (0 or 1), it is essentially
an analog device. The capacitor can store any charge value within a range; a threshold
value determines whether the charge is interpreted as 1 or 0.

## Slide 7: Static RAM (SRAM)
  Digital device that uses the same logic elements used in the processor
  Binary values are stored using traditional flip-flop logic gate configurations
  Will hold its data as long as power is supplied to it
Notes: In contrast, a static RAM (SRAM) is a digital device that uses the
same logic elements used in the processor. In a SRAM, binary values are stored
using traditional flip-flop logic-gate configurations (see Chapter 11 for a description
of flip-flops). A static RAM will hold its data as long as power is supplied to it.

## Slide 8: Static RAM Structure
Figure 5.2b
Typical Memory Cell Structures
Notes: Figure 5.2b is a typical SRAM structure for an individual cell. Four transistors
(T1, T2, T3, T4) are cross connected in an arrangement that produces a stable logic
state. In logic state 1, point C1 is high and point C2 is low; in this state, T1 and T4 are off
and T2 and T3 are on. In logic state 0, point C1 is low and point C2 is high; in this state,
T1 and T4 are on and T2 and T3 are off. Both states are stable as long as the direct
current (dc) voltage is applied. Unlike the DRAM, no refresh is needed to retain data.
As in the DRAM, the SRAM address line is used to open or close a switch.
The address line controls two transistors (T5 and T6). When a signal is applied to
this line, the two transistors are switched on, allowing a read or write operation. For
a write operation, the desired bit value is applied to line B, while its complement
is applied to line B. This forces the four transistors (T1, T2, T3, T4) into the proper
state. For a read operation, the bit value is read from line B.

## Slide 9: SRAM versus DRAM
Both volatile
  Power must be continuously supplied to the memory to preserve the bit values
Dynamic cell
  Simpler to build, smaller
  More dense (smaller cells = more cells per unit area)
  Less expensive
  Requires the supporting refresh circuitry
  Tend to be favored for large memory requirements
  Used for main memory
Static
  Faster
  Used for cache memory (both on and off chip)
SRAM
DRAM
Notes: Both static and dynamic RAMs are volatile; that is,
power must be continuously supplied to the memory to preserve the bit values.
A dynamic memory cell is simpler and smaller than a static memory cell. Thus, a
DRAM is more dense (smaller cells = more cells per unit area) and less expensive
than a corresponding SRAM. On the other hand, a DRAM requires the supporting
refresh circuitry. For larger memories, the fixed cost of the refresh circuitry is more
than compensated for by the smaller variable cost of DRAM cells. Thus, DRAMs
tend to be favored for large memory requirements. A final point is that SRAMs are
somewhat faster than DRAMs. Because of these relative characteristics, SRAM is
used for cache memory (both on and off chip), and DRAM is used for main memory.

## Slide 10: Read Only Memory (ROM)
Contains a permanent pattern of data that cannot be changed or added to
No power source is required to maintain the bit values in memory
Data or program is permanently in main memory and never needs to be loaded from a secondary storage device
Data is actually wired into the chip as part of the fabrication process
  Disadvantages of this:
    No room for error, if one bit is wrong the whole batch of ROMs must be thrown out
    Data insertion step includes a relatively large fixed cost
Notes: As the name suggests, a read-only memory (ROM) contains a permanent pattern
of data that cannot be changed. A ROM is nonvolatile; that is, no power source is
required to maintain the bit values in memory. While it is possible to read a ROM,
it is not possible to write new data into it. An important application of ROMs is
microprogramming, discussed in Part Four. Other potential applications include
• Library subroutines for frequently wanted functions
• System programs
• Function tables
For a modest-sized requirement, the advantage of ROM is that the data or program
is permanently in main memory and need never be loaded from a secondary storage
device.
A ROM is created like any other integrated circuit chip, with the data actually
wired into the chip as part of the fabrication process. This presents two problems:
• The data insertion step includes a relatively large fixed cost, whether one or
thousands of copies of a particular ROM are fabricated.
• There is no room for error. If one bit is wrong, the whole batch of ROMs must
be thrown out.

## Slide 11: Programmable ROM (PROM)
Less expensive alternative
Nonvolatile and may be written into only once
Writing process is performed electrically and may be performed by supplier or customer at a time later than the original chip fabrication
Special equipment is required for the writing process
Provides flexibility and convenience
Attractive for high volume production runs
Notes: When only a small number of ROMs with a particular memory content is
needed, a less expensive alternative is the programmable ROM (PROM). Like the
ROM, the PROM is nonvolatile and may be written into only once. For the PROM,
the writing process is performed electrically and may be performed by a supplier
or customer at a time later than the original chip fabrication. Special equipment is
required for the writing or “programming” process. PROMs provide flexibility and
convenience. The ROM remains attractive for high-volume production runs.

## Slide 12: Read-Mostly Memory
EPROM
Erasable programmable read-only memory
Erasure process can be performed repeatedly
More expensive than PROM but it has the advantage of the multiple update capability
EEPROM
Electrically erasable programmable read-only memory
Can be written into at any time without erasing prior contents
Combines the advantage of non-volatility with the flexibility of being updatable in place
More expensive than EPROM
Flash Memory
Intermediate between EPROM and EEPROM in both cost and functionality
Uses an electrical erasing technology, does not provide byte-level erasure
Microchip is organized so that a section of memory cells are erased in a single action or “flash”
Notes: Another variation on read-only memory is the read-mostly memory, which is
useful for applications in which read operations are far more frequent than write
operations but for which nonvolatile storage is required. There are three common
forms of read-mostly memory: EPROM, EEPROM, and flash memory.
The optically erasable programmable read-only memory (EPROM) is read
and written electrically, as with PROM. However, before a write operation, all the
storage cells must be erased to the same initial state by exposure of the packaged
chip to ultraviolet radiation. Erasure is performed by shining an intense ultraviolet
light through a window that is designed into the memory chip. This erasure process
can be performed repeatedly; each erasure can take as much as 20 minutes to
perform. Thus, the EPROM can be altered multiple times and, like the ROM and
PROM, holds its data virtually indefinitely. For comparable amounts of storage, the
EPROM is more expensive than PROM, but it has the advantage of the multiple
update capability.
A more attractive form of read-mostly memory is electrically erasable programmable
read-only memory (EEPROM). This is a read-mostly memory that can
be written into at any time without erasing prior contents; only the byte or bytes
addressed are updated. The write operation takes considerably longer than the read
operation, on the order of several hundred microseconds per byte. The EEPROM
combines the advantage of non-volatility with the flexibility of being updatable in
place, using ordinary bus control, address, and data lines. EEPROM is more expensive
than EPROM and also is less dense, supporting fewer bits per chip.
Another form of semiconductor memory is flash memory (so named because
of the speed with which it can be reprogrammed). First introduced in the mid-1980s,
flash memory is intermediate between EPROM and EEPROM in both cost and
functionality. Like EEPROM, flash memory uses an electrical erasing technology.
An entire flash memory can be erased in one or a few seconds, which is much faster
than EPROM. In addition, it is possible to erase just blocks of memory rather than
an entire chip. Flash memory gets its name because the microchip is organized so
that a section of memory cells are erased in a single action or “flash.” However,
flash memory does not provide byte-level erasure. Like EPROM, flash memory
uses only one transistor per bit, and so achieves the high density (compared with
EEPROM) of EPROM.

## Slide 13: Typical 16 Mb DRAM (4M x 4)
Notes: Figure 5.3 shows a typical organization of a 16-Mbit DRAM. In this case, 4 bits
are read or written at a time. Logically, the memory array is organized as four square
arrays of 2048 by 2048 elements. Various physical arrangements are possible. In any
case, the elements of the array are connected by both horizontal (row) and vertical
(column) lines. Each horizontal line connects to the Select terminal of each cell in its
row; each vertical line connects to the Data-In/Sense terminal of each cell in its column.
Address lines supply the address of the word to be selected. A total of log2 W
lines are needed. In our example, 11 address lines are needed to select one of 2048
rows. These 11 lines are fed into a row decoder, which has 11 lines of input and 2048
lines for output. The logic of the decoder activates a single one of the 2048 outputs
depending on the bit pattern on the 11 input lines (211 = 2048).
An additional 11 address lines select one of 2048 columns of 4 bits per column.
Four data lines are used for the input and output of 4 bits to and from a data buffer.
On input (write), the bit driver of each bit line is activated for a 1 or 0 according to
the value of the corresponding data line. On output (read), the value of each bit line
is passed through a sense amplifier and presented to the data lines. The row line
selects which row of cells is used for reading or writing.
Because only 4 bits are read/written to this DRAM, there must be multiple
DRAMs connected to the memory controller to read/write a word of data to the bus.
Note that there are only 11 address lines (A0–A10), half the number you
would expect for a 2048 * 2048 array. This is done to save on the number of pins.
The 22 required address lines are passed through select logic external to the chip
and multiplexed onto the 11 address lines. First, 11 address signals are passed to the
chip to define the row address of the array, and then the other 11 address signals are
presented for the column address.
As an aside, multiplexed addressing plus the use of square arrays result in a
quadrupling of memory size with each new generation of memory chips. One more
pin devoted to addressing doubles the number of rows and columns, and so the size
of the chip memory grows by a factor of 4.
Figure 5.3 also indicates the inclusion of refresh circuitry. All DRAMs require
a refresh operation. A simple technique for refreshing is, in effect, to disable the
DRAM chip while all data cells are refreshed. The refresh counter steps through all
of the row values. For each row, the output lines from the refresh counter are supplied
to the row decoder and the RAS line is activated. The data are read out and
written back into the same location. This causes each cell in the row to be refreshed.

## Slide 14: Chip Packaging
Notes: As was mentioned in Chapter 2, an integrated circuit is mounted on a package that
contains pins for connection to the outside world.
Figure 5.4a shows an example EPROM package, which is an 8-Mbit chip
organized as 1M * 8. In this case, the organization is treated as a one-word-per-chip
package. The package includes 32 pins, which is one of the standard chip package
sizes. The pins support the following signal lines:
• The address of the word being accessed. For 1M words, a total of 20 (220 = 1M)
pins are needed (A0–A19).
• The data to be read out, consisting of 8 lines (D0–D7).
• The power supply to the chip (Vcc).
• A ground pin (Vss).
• A chip enable (CE) pin. Because there may be more than one memory chip,
each of which is connected to the same address bus, the CE pin is used to indicate
whether or not the address is valid for this chip. The CE pin is activated
by logic connected to the higher-order bits of the address bus (i.e., address bits
above A19). The use of this signal is illustrated presently.
• A program voltage (Vpp) that is supplied during programming (write operations).
A typical DRAM pin configuration is shown in Figure 5.4b, for a 16-Mbit chip
organized as 4M * 4. There are several differences from a ROM chip. Because
a RAM can be updated, the data pins are input/output. The write enable (WE)
and output enable (OE) pins indicate whether this is a write or read operation.
Because the DRAM is accessed by row and column, and the address is multiplexed,
only 11 address pins are needed to specify the 4M row/column combinations
(211 * 211 = 222 = 4M). The functions of the row address select (RAS) and column
address select (CAS) pins were discussed previously. Finally, the no connect (NC)
pin is provided so that there are an even number of pins.

## Slide 15
Figure 5.5
256-KByte
Memory
Organization
Notes: If a RAM chip contains only 1 bit per word, then clearly we will need at least a
number of chips equal to the number of bits per word. As an example, Figure 5.5
shows how a memory module consisting of 256K 8-bit words could be organized. For
256K words, an 18-bit address is needed and is supplied to the module from some
external source (e.g., the address lines of a bus to which the module is attached).
The address is presented to 8 256K * 1-bit chips, each of which provides the input/
output of 1 bit.

## Slide 16: 1MByte Module Organization
Notes: This organization works as long as the size of memory equals the number of
bits per chip. In the case in which larger memory is required, an array of chips is
needed. Figure 5.6 shows the possible organization of a memory consisting of 1M
word by 8 bits per word. In this case, we have four columns of chips, each column
containing 256K words arranged as in Figure 5.5. For 1M word, 20 address lines are
needed. The 18 least significant bits are routed to all 32 modules. The high-order
2 bits are input to a group select logic module that sends a chip enable signal to one
of the four columns of modules.

## Slide 17: Interleaved Memory
Composed of a collection of DRAM chips
Grouped together to form a memory bank
Each bank is independently able to service a memory read or write request
K banks can service K requests simultaneously, increasing memory read or write rates by a factor of K
If consecutive words of memory are stored in different banks, the transfer of a block of memory is speeded up
Notes: Main memory is composed of a collection of DRAM memory chips. A number of
chips can be grouped together to form a memory bank. It is possible to organize
the memory banks in a way known as interleaved memory. Each bank is independently
able to service a memory read or write request, so that a system with
K banks can service K requests simultaneously, increasing memory read or write
rates by a factor of K. If consecutive words of memory are stored in different
banks, then the transfer of a block of memory is speeded up. Appendix E explores
the topic of interleaved memory.

## Slide 18: Error Correction
Hard Failure
  Permanent physical defect
  Memory cell or cells affected cannot reliably store data but become stuck at 0 or 1 or switch erratically between 0 and 1
  Can be caused by:
    Harsh environmental abuse
    Manufacturing defects
    Wear
Soft Error
  Random, non-destructive event that alters the contents of one or more memory cells
  No permanent damage to memory
  Can be caused by:
    Power supply problems
    Alpha particles
Notes: A semiconductor memory system is subject to errors. These can be categorized as
hard failures and soft errors. A hard failure is a permanent physical defect so that
the memory cell or cells affected cannot reliably store data but become stuck at
0 or 1 or switch erratically between 0 and 1. Hard errors can be caused by harsh
environmental abuse, manufacturing defects, and wear. A soft error is a random,
nondestructive event that alters the contents of one or more memory cells without
damaging the memory. Soft errors can be caused by power supply problems
or alpha particles. These particles result from radioactive decay and are distressingly
common because radioactive nuclei are found in small quantities in nearly all
materials. Both hard and soft errors are clearly undesirable, and most modern main
memory systems include logic for both detecting and correcting errors.

## Slide 19: Error Correcting Code Function
Notes: Figure 5.7 illustrates in general terms how the process is carried out. When
data are to be written into memory, a calculation, depicted as a function f, is performed
on the data to produce a code. Both the code and the data are stored. Thus,
if an M-bit word of data is to be stored and the code is of length K bits, then the
actual size of the stored word is M + K bits.
When the previously stored word is read out, the code is used to detect and possibly
correct errors. A new set of K code bits is generated from the M data bits and
compared with the fetched code bits. The comparison yields one of three results:
• No errors are detected. The fetched data bits are sent out.
• An error is detected, and it is possible to correct the error. The data bits plus
error correction bits are fed into a corrector, which produces a corrected set of
M bits to be sent out.
• An error is detected, but it is not possible to correct it. This condition is reported.
Codes that operate in this fashion are referred to as error-correcting codes. A
code is characterized by the number of bit errors in a word that it can correct and detect.

## Slide 20: Hamming Error Correcting Code
Notes: The simplest of the error-correcting codes is the Hamming code devised by
Richard Hamming at Bell Laboratories. Figure 5.8 uses Venn diagrams to illustrate
the use of this code on 4-bit words (M = 4). With three intersecting circles,
there are seven compartments. We assign the 4 data bits to the inner compartments
(Figure5.8a). The remaining compartments are filled with what are called parity
bits. Each parity bit is chosen so that the total number of 1s in its circle is even
(Figure5.8b). Thus, because circle A includes three data 1s, the parity bit in that
circle is set to 1. Now, if an error changes one of the data bits (Figure 5.8c), it is easily
found. By checking the parity bits, discrepancies are found in circle A and circle
C but not in circle B. Only one of the seven compartments is in A and C but not B.
The error can therefore be corrected by changing that bit.

## Slide 21: Layout of Data Bits and Check Bits
Notes: To achieve these characteristics, the data and check bits are arranged into a
12-bit word as depicted in Figure 5.9. The bit positions are numbered from 1 to 12.
Those bit positions whose position numbers are powers of 2 are designated as check
bits.

## Slide 22
Notes: Figure 5.10 illustrates the calculation. The data and check bits are
positioned properly in the 12-bit word. Four of the data bits have a value 1 (shaded
in the table), and their bit position values are XORed to produce the Hamming
code 0111, which forms the four check digits. The entire block that is stored is
001101001111. Suppose now that data bit 3, in bit position 6, sustains an error and is
changed from 0 to 1. The resulting block is 001101101111, with a Hamming code of
0111. An XOR of the Hamming code and all of the bit position values for nonzero
data bits results in 0110. The nonzero result detects an error and indicates that the
error is in bit position 6.

## Slide 23: Check Bit Calculation
Notes: Figure 5.10 illustrates the calculation. The data and check bits are
positioned properly in the 12-bit word. Four of the data bits have a value 1 (shaded
in the table), and their bit position values are XORed to produce the Hamming
code 0111, which forms the four check digits. The entire block that is stored is
001101001111. Suppose now that data bit 3, in bit position 6, sustains an error and is
changed from 0 to 1. The resulting block is 001101101111, with a Hamming code of
0111. An XOR of the Hamming code and all of the bit position values for nonzero
data bits results in 0110. The nonzero result detects an error and indicates that the
error is in bit position 6.

## Slide 24: Hamming SEC-DED Code
Notes: The code just described is known as a single-error-correcting (SEC) code.
More commonly, semiconductor memory is equipped with a single-error-correcting,
double-error-detecting (SEC-DED) code. As Table 5.2 shows, such codes require
one additional bit compared with SEC codes.
Figure 5.11 illustrates how such a code works, again with a 4-bit data word.
The sequence shows that if two errors occur (Figure 5.11c), the checking procedure
goes astray (d) and worsens the problem by creating a third error (e). To overcome
the problem, an eighth bit is added that is set so that the total number of 1s in the
diagram is even. The extra parity bit catches the error (f).
An error-correcting code enhances the reliability of the memory at the cost of
added complexity. With a 1-bit-per-chip organization, an SEC-DED code is generally
considered adequate. For example, the IBM 30xx implementations used an 8-bit SECDED
code for each 64 bits of data in main memory. Thus, the size of main memory is
actually about 12% larger than is apparent to the user. The VAX computers used a 7-bit
SEC-DED for each 32 bits of memory, for a 22% overhead. A number of contemporary
DRAMs use 9 check bits for each 128 bits of data, for a 7% overhead [SHAR97].

## Slide 25: Summary
Semiconductor main memory
  Organization
  DRAM and SRAM
  Types of ROM
  Chip logic
  Chip packaging
  Module organization
  Interleaved memory
Error correction
  Hard failure
  Soft error
  Hamming code
  Advanced DRAM organization
  Synchronous DRAM
  Rambus DRAM
  DDR SDRAM
  Cache DRAM
Chapter 5
Internal
Memory
Notes: Chapter 5 summary.

## Slide 26: Key terms
semiconductor memory
nonvolatile memory
read-mostly memory
read-only memory (ROM)
programmable ROM (PROM)
erasable programmable ROM (EPROM)
electrically erasable programmable ROM (EEPROM)
dynamic RAM (DRAM)
static RAM (SRAM)
flash memory
volatile memory
error correcting code (ECC)
error correction
syndrome
Hamming code
hard failure
soft error
single-error-correcting (SEC) code
single-error-correcting, double-error-detecting (SEC-DED) code
Chapter 5

## Slide 27: Homework
5.2
5.3
5.6
5.7
5.10-14
Chapter 5